## Slide 1: N_parallel_Sinlge_data_Analysis
코드 분석
# Updated 2024-0315 HHWI
# CST 2024 sp2 version
# Imported data format for singlecase only
# Default, Power and Normalized (0, 1)
# Default Plot range, -15 to 15
# Stored directory should be changed before run, Default is Z:\\data_save
주석

## Slide 2: N_parallel_Sinlge_data_Analysis
모듈 선언
Import pandas as pd
import numpy as np
Import matplotlib.pyplot as plt
from scipy.fft import fft, fftfreq, fftshift
from scipy.signal import find_peaks
from scipy.integrate import simpson
from tkinter import Tk
from tkinter.filedialog import askopenfilename
import os
줄임말 설정
scipy, tkinter: 패키지
fft, signal, itegrate: scipy 안에 있는 모듈
Tk, filedialog: tkinter 안에 있는 모듈
fft, fftfreq, fftshift, find_peaks, simpson, askopenfilename :
앞으로 올 코드에서 추가 선언 없이 사용할 모듈 안의 함수들

## Slide 3: N_parallel_Sinlge_data_Analysis
def 함수(매개 변수) 선언
함수1 선언
#, “””: 주석 표현, 앞으로 초록으로 표시
상수 설정(코드 내에서 값 바뀌지 X)
# Constants
FREQ = 476e6 # Frequency in MHz
C = 2.998e8 # Speed of light in m/s
save_directory = "Z:\\data_save"
PROCESSING_RANGE = (-15, 15) # Processing range: [-15, 15]
def load_data(file_path):
"""Load data from a file."""
return pd.read_csv(file_path, comment='#', delimiter='\t', header=None, names=['Length_mm', 'Re_V/m', 'Im_V/m'])

## Slide 4: N_parallel_Sinlge_data_Analysis
함수2 선언
def process_signal(data, freq=FREQ, c=C):
"""Process the signal and return FFT result and directivity."""
complex_signal = data['Re_V/m'].to_numpy() + 1j * data['Im_V/m'].to_numpy()
N = len(complex_signal)
sample_spacing = (data['Length_mm'].iloc[-1] - data['Length_mm'].iloc[0]) / (N - 1) * 1e-3
N_nn = 50 * 2**np.ceil(np.log2(N)).astype(int)
fft_result_nn = fft(complex_signal, n=N_nn)
fft_result_shifted_nn = fftshift(fft_result_nn)
fft_result_shifted_magnitude_nn = np.abs(fft_result_shifted_nn)
fft_result_shifted_magnitude_normalized_nn = fft_result_shifted_magnitude_nn / np.max(fft_result_shifted_magnitude_nn)
spectrum = fft_result_shifted_magnitude_normalized_nn ** 2
n_nn, spectrum 출력하기 위한 함수
지역 변수 설정
spectrum 정의

## Slide 5: N_parallel_Sinlge_data_Analysis
함수2 선언 (process_signal 함수 앞에 이어서 )
frequencies_nn = fftshift(fftfreq(N_nn, d=sample_spacing))
n_nn = frequencies_nn * c / freq
return n_nn, spectrum
코드 처음에 호출했던 fftshift, fftfreq 함수들로 frequencies_nn 정의,
해당 변수로 n_nn 정의
함수3 선언
def calculate_directivity(n_nn, spectrum):
mask_full_range = (n_nn >= PROCESSING_RANGE[0]) & (n_nn <= PROCESSING_RANGE[1])
mask_partial_range = (n_nn >= 2) & (n_nn <= 4)
integral_full_range = simpson(y=spectrum[mask_full_range], x=n_nn[mask_full_range])
integral_partial_range = simpson(y=spectrum[mask_partial_range], x=n_nn[mask_partial_range])
return (integral_partial_range / integral_full_range) * 100
앞에서 만든 n_nn, spectrum 을 매개 변수로 사용
이 함수의 결과물: (integral_partial_range / integral_full_range) * 100
simpson: 코드 맨 앞에서 호출한 함수

## Slide 6: N_parallel_Sinlge_data_Analysis
함수4 선언
그래프 시각화(생성) 함수, find peaks 함수는 맨 앞에서 정의
def plot_spectrum(n_nn, power_spectrum, directivity):
"""Plot the spectrum, annotate directivity and the top two peaks."""
plt.figure(figsize=(10, 6), dpi=200)
plt.plot(n_nn, power_spectrum, label='Power Spectrum')
peaks, _ = find_peaks(power_spectrum, height=0) # Find peaks in the power spectrum
valid_peaks = (n_nn[peaks] >= PROCESSING_RANGE[0]) & (n_nn[peaks] <= PROCESSING_RANGE[1])
# Filter peaks to those within the plot range(앞 코드)
peak_freqs = n_nn[peaks][valid_peaks]
peak_powers = power_spectrum[peaks][valid_peaks]
# Sort peaks by power and select the top two
sorted_indices = np.argsort(peak_powers)[::-1][:2] # Change here to adjust the number of top peaks
top_peaks_freqs = peak_freqs[sorted_indices]
top_peaks_powers = peak_powers[sorted_indices]
뒤에 이어서…
정의되지 않은 변수, 함수 호출 시 제대로 넣어줘야 함

## Slide 7: N_parallel_Sinlge_data_Analysis
함수4 선언 (plot_spectrum 함수 앞에 이어서 )
# Annotate the top two peaks on the plot
for i, (freq, power) in enumerate(zip(top_peaks_freqs, top_peaks_powers)):
plt.annotate(f'Peak {i + 1}: ({freq:.2f}, {power:.2f})', (freq, power),
textcoords="offset points", xytext=(5, -12), ha='center', color='red')
plt.text(-9, max(power_spectrum) * 0.9, f'Directivity: {directivity:.2f}%', color='blue')
# Directivity annotation(앞 코드)
plt.title('Parallel Refractive Index Power Spectrum')
plt.xlabel('Refractive Index (n)')
plt.ylabel('Power Spectrum')
plt.xlim([PROCESSING_RANGE[0], PROCESSING_RANGE[1]])
plt.ylim([0, 1])
plt.grid(True)
plt.legend()
plt.show()
Power spectrum(y축) vs n||(x축) 그래프 출력

## Slide 8: N_parallel_Sinlge_data_Analysis
함수5 선언
def save_data(n_nn, spectrum):
os.makedirs(save_directory, exist_ok=True) # Ensure the directory exists
filter_mask = (n_nn >= PROCESSING_RANGE[0]) & (n_nn <= PROCESSING_RANGE[1])
# Filter the data for the range -10 to 10(앞 코드)
n_nn_filtered = n_nn[filter_mask]
spectrum_filtered = spectrum[filter_mask]
fft_data_path = os.path.join(save_directory, f"Power_Spectrum.csv")
with open(fft_data_path, 'w', newline='') as file: # Ensures no extra newline characters
pd.DataFrame({'n_nn': n_nn_filtered, 'spectrum': spectrum_filtered}).to_csv(file, index=False)
print(f"FFT spectrum data saved to {fft_data_path}")
함수6 선언
def select_file():
"""Open a file dialog for the user to select a file."""
Tk().withdraw() # we don't want a full GUI, so keep the root window from appearing
filename = askopenfilename(filetypes=[("Text files", "*.txt")], initialdir="Z:\\data")
# Show an "Open" dialog box and return the path to the selected file
return filename
TK(), askopenfilename = 코드 맨 처음에 호출한 모듈과 함수

## Slide 9: N_parallel_Sinlge_data_Analysis
def main():
"""Main function to process signal data and plot results."""
file_path = select_file() # Use the GUI to get the file path
if file_path: # Proceed only if a file was selected
data = load_data(file_path)
n_nn, spectrum = process_signal(data)
directivity = calculate_directivity(n_nn, spectrum)
print(f"Directivity(%): {directivity:.2f}%")
plot_spectrum(n_nn, spectrum, directivity)
save_data(n_nn, spectrum)
else:
print("No file selected.")
if __name__ == "__main__":
main()
함수7 선언
load_data:
코드에서 만든 1번 함수
n_nn, spectrum: 2번
함수에서 정의한 변수
Print문의 f: 문자열 의미
.2f : 소수점 이하 두
자리까지 출력
plot_spectrum :
코드에서 만든 4번 함수
파일 선택해서 그래프 출력하는 메인 코드
save_data:
코드에서 만든 5번 함수
calculate_directivity :
코드에서 만든 3번 함수
select_file() :
코드에서 만든 6번 함수